## Slide 1: Corner-Based Estimation of Tire Forces
Presented by: Brian Mao
Prepared for: Stephen Smith
ECE 686: Filtering and Control of Stochastic Linear Systems
Corner-Based Estimation of Tire Forces and Vehicle Velocities Robust to Road Conditions (2017)
Ehsan Hashemi, Mohammad Pirani, Amir Khajepour, Alireza Kasaiezadeh, Shih-Ken Chen, Bakhtiar Litkouhi

## Slide 2: Vehicle Control Systems
Other Examples:
Anti-Lock Braking System
Active Steering
Differential Braking
Makes Driving Safer and Easier
Required for Fully Autonomous Driving

## Slide 3: Driving Under Poor Weather Conditions

## Slide 4: Controller Design
Problem:
Automotive companies currently spend a large amount of money and time to develop and tune controllers for new vehicles
Goal:
Reduce the development time for new vehicles by designing controllers that are universal to any vehicle configuration

## Slide 5: Corner-Based Estimation
Universal Estimation Approach
Direct Measurement is Impractical on Mass Production Vehicles

## Slide 6: Lateral Force Estimation
Estimated using Unscented Kalman Filter (UKF)
State
Outputs

## Slide 7: Unscented Kalman Filter (UKF)
Main Idea: It is easier to approximate a probability distribution compared to a nonlinear function
An unscented transform is a function that estimates the result of applying a non-linear function on a probability density function given a finite set of samples
Greater accuracy than an Extended Kalman Filter (EKF) for highly non-linear systems

## Slide 8: Overview
System Model:
Measurement/Output Model:
Initialization:
Followed by Prediction and Correction Stages

## Slide 9: Prediction: Sigma Point Generation
2. Sigma Point Parameters
1. Cholesky Decomposition of Covariance Matrix:
Generate 2N+1 sigma points (where N = Length of State Vector)
3. Sigma Point Generation

## Slide 10: Prediction: Propagate Sigma Points

## Slide 11: Prediction: Mean and Covariance Calculation
Mean Calculation:
Covariance Calculation:
Weighting Terms for Mean
Weighting Terms for Covariance

## Slide 12: Correction: Sigma Point Generation
2. Sigma Point Parameters (Same as Prediction Step)
1. Cholesky Decomposition of State Covariance Matrix:
Generate another 2N+1 sigma points (where N = Length of State Vector)
3. Sigma Point Generation

## Slide 13: Correction: Propagate Sigma Points + Mean + Covariance
(Same Weighting Parameters as Prediction Stage)
Mean Calculation:
Covariance Calculation:

## Slide 14: State and Covariance Update
Cross Covariance Calculation:
Kalman Gain:
State Update:
Covariance Update:

## Slide 15: Unscented Kalman Filter (UKF) Summary Part 1
Prediction Step
Sigma Point Generation (
Initialization

## Slide 16: Unscented Kalman Filter (UKF) Summary Part 2
Correction Step
Sigma Point Generation ()
Cross-Covariance + Kalman Gain
Update

## Slide 17: Experimental Test Data
Longitudinal Acceleration (X-Direction)
Lateral Acceleration (Y-Direction)
Yaw Rate
Wheel Speeds
Wheel Torques

## Slide 18: Harsh Lane Change Maneuver

## Slide 19: Harsh Steering Maneuver on Icy Road to Packed Snow

## Slide 20: Simulation Results Summary
Paper Results (Figure 8)
Simulation Results (MATLAB)

## Slide 21: Parameter Estimation Problem
Implementation is a modified version of the state estimation problem presented since no dynamic model with forces are developed in the paper
Initialization
Prediction Step
Same Sigma Point Generation (

## Slide 22: Parameter Estimation Problem
Correction Step
Cross-Covariance + Kalman Gain
Update

## Slide 23: Conclusion
Lateral Force Estimation using Unscented Kalman Filter (UKF)
UKF

## Slide 24: Corner-based Estimation of Tire Forces

## Slide 25: Supplementary Slides

## Slide 26: Longitudinal Force
Parameter | Value | Description
 | 0.33 m | Effective Radius
 | 1.68 kg m2 | Wheel Moment of Inertia
 | Measured | Total Effective Torque
 | Calculated From Measured Wheel Speed | Wheel Acceleration
Parameter | Value | Description
 | 0.33 m | Effective Radius
 | 1.68 kg m2 | Wheel Moment of Inertia
 | Measured | Total Effective Torque
 | Calculated From Measured Wheel Speed | Wheel Acceleration

## Slide 27: Other Vehicle Parameters
Parameter | Value | Description
m | 2270 kg | Vehicle Mass
Iz | 4650 kg m2 | Vehicle Moment of Inertia
Lf | 1.42 m | Front Axle to Center of Gravity Distance
Trf | 1.62 m | Front Track Width
Trr | 1.56 m | Rear Track Width
 | Measured | Steering Angle
Parameter | Value | Description
m | 2270 kg | Vehicle Mass
Iz | 4650 kg m2 | Vehicle Moment of Inertia
Lf | 1.42 m | Front Axle to Center of Gravity Distance
Trf | 1.62 m | Front Track Width
Trr | 1.56 m | Rear Track Width
 | Measured | Steering Angle
Variable | Calculation
Variable | Calculation

## Slide 28: System and Measurement Models
Where for each time step k:
Process Uncertainty:
Measurement Uncertainty:

## Slide 29: Observability of the System
The observability matrix of the system is given by:
where
Note that rank () = 3 for the operating regions of the steering angle and its time derivatives except when or for
For , the lateral force is equal to zero
Situations of do not occur since the maximum value of the steering angle is much less than on commercial vehicles
Therefore the system is observable, which is a sufficient condition for the implementation of an optimal variance estimator (Such as a Kalman estimator)

## Slide 30: General Comparison Between State Estimators
State Estimator | Model | Computational Cost
Kalman Filter (KF) | Linear | Low
Extended Kalman Filter (EKF) | Locally Linear | Low (For analytically computed Jacobians) Medium (For numerically computed Jacobians)
Unscented Kalman Filter (UKF) | Nonlinear | Medium
Particle Filter (PF) | Nonlinear | High

## Slide 31: Disclaimer on Available Experimental Data
Note that the experimental data used to generate Figures 6 and 7 were not available from the main author of the paper (Ehsan Hashemi)
However, data for the longitudinal forces was still available for Figure 8 (Harsh Steering on Icy Road to Packed Snow)

## Slide 32: Measurement Equipment
RT2500 6-Axis GPS
IMU
Wheel Speed Sensors
CAN-bus for communication
Sampling Frequency of 200 Hz

## Slide 33: Acceleration Measurements
Note: Test data collected for Figure 8 was conducted on a flat surface (Pitch, Roll, Road Grade, and Bank Angles are all Zero) and
Corrected Acceleration Measurements:
Road Grade Angle
Bank Angle
Roll Angle
Pitch Angle

## Slide 34: Extensions Beyond Lateral Force Estimation
The developed lateral tire force estimator is utilized in a corner-based approach for vehicle velocity estimation later in the paper
The velocity estimation method also requires a road grade estimator developed in a previous paper, as well as a vertical tire force estimator developed following the lateral force estimation
Road condition classification is another result from the overall corner-based estimation approach independent from lateral force estimation

## Slide 35: References
Videos
Do you really need awd in the snow? [Video file]. (2015, September 15). Retrieved April 11, 2021, from https://www.consumerreports.org/cro/magazine/2015/09/do-you-really-need-awd-in-the-snow/index.htm
Khajepour, A. (Director). (2021, February 08). Holistic vehicle control [Video file]. Retrieved April 11, 2021, from https://uwaterloo.ca/mechatronic-vehicle-systems-lab/research/vehicle-control-systems/holistic-vehicle-control
Robinson, D. (Director). (2016, October 17). How to correct a slide on an icy road (and how to prevent them) - Winter driving education [Video file]. Retrieved April 11, 2021, from https://www.youtube.com/watch?v=TZQXuWzBC18
Resources
Ehsan Hashemi (2017). Full Vehicle State Estimation Using a Holistic Corner-based Approach. UWSpace. http://hdl.handle.net/10012/11744
Ehsan Hashemi, Mohammad Pirani, Amir Khajepour, Alireza Kasaiezadeh, Shih-Ken Chen, Bakhtiar Litkouhi, Corner-based estimation of tire forces and vehicle velocities robust to road conditions, Control Engineering Practice, Volume 61, 2017, Pages 28-40, ISSN 0967-0661, https://doi.org/10.1016/j.conengprac.2017.01.009.
Kelly, J. (Director). (2021). An alternative to the ekf - The Unscented Kalman filter - Module 2: State estimation - linear and Nonlinear Kalman filters [Video file]. Retrieved April 11, 2021, from https://www.coursera.org/lecture/state-estimation-localization-self-driving-cars/lesson-6-an-alternative-to-the-ekf-the-unscented-kalman-filter-voRRb
Images
Dollar Sign Clipart [Digital image]. (2019). Retrieved April 11, 2021, from http://clipart-library.com/clip-art/25-259936_ecmhva-dollar-sign-png-transparent.htm
Ehsan Hashemi, Mohammad Pirani, Amir Khajepour, Alireza Kasaiezadeh, Shih-Ken Chen, Bakhtiar Litkouhi, Corner-based estimation of tire forces and vehicle velocities robust to road conditions, Control Engineering Practice, Volume 61, 2017, Pages 28-40, ISSN 0967-0661, https://doi.org/10.1016/j.conengprac.2017.01.009.
Guillaume Baffet, Ali Charara, Daniel Lechner, Estimation of vehicle sideslip, tire force and wheel cornering stiffness, Control Engineering Practice, Volume 17, Issue 11, 2009, Pages 1255-1264, ISSN 0967-0661, https://doi.org/10.1016/j.conengprac.2009.05.005.
H. Fang, N. Tian, Y. Wang, M. Zhou and M. A. Haile, "Nonlinear Bayesian estimation: from Kalman filtering to a broader horizon," in IEEE/CAA Journal of Automatica Sinica, vol. 5, no. 2, pp. 401-417, Mar. 2018, doi: 10.1109/JAS.2017.7510808.
Kelly, J. (Director). (2021). An alternative to the ekf - The Unscented Kalman filter - Module 2: State estimation - linear and Nonlinear Kalman filters [Video file]. Retrieved April 11, 2021, from https://www.coursera.org/lecture/state-estimation-localization-self-driving-cars/lesson-6-an-alternative-to-the-ekf-the-unscented-kalman-filter-voRRb
Khajepour, A. (2021). Mechatronic Vehicle Systems Lab [Digital image]. Retrieved April 11, 2021, from https://uwaterloo.ca/mechatronic-vehicle-systems-lab/
Namm, M. (2020). ADAS (Advanced Driver Assistance Systems) [Digital image]. Retrieved April 11, 2021, from https://learn.sonicelectronix.com/advanced-driver-assistance-systems/
R. (2019, October 19). The 10 Best And Worst Car Brands In The Automotive Industry [Digital image]. Retrieved April 11, 2021, from https://autowise.com/car-brands/